## Slide 1: Stormwater Management Rules Applicability and Amendments
Gabriel Mahon, Bureau Chief
Bureau of Nonpoint Pollution Control
Division of Water Quality
New Jersey Department of Environmental Protection

## Slide 2: How is post-construction stormwater managed in NJ?
Stormwater Management rules at N.J.A.C. 7:8
  Compliance required through permits issued by the Division of Land Use Regulation
    Direct Implementation by NJDEP
  Compliance required through MS4 Permits issued by the Bureau of Nonpoint Pollution Control in the Division of Water Quality
    Implementation by municipality
      RSIS for residential projects
      Stormwater Control Ordinance for non-residential projects

## Slide 3: What projects must comply?
“Major Development”
Under existing rules:
  If reviewed by NJDEP – any development or developments that ultimately disturb one acre or more of land or create ¼ acre or more increase of impervious surface
  If reviewed by the municipality
    Through RSIS – ultimate disturbance of one acre or more
    Through Stormwater Ordinance – as defined in ordinance (but must at least cover projects that where the ultimate disturbance is one acre or more)

## Slide 4: Proposed Amendments to Stormwater Management rules
Dec. 3, 2018: NJDEP proposed amendments to the Stormwater Management rules.
Feb. 1, 2019: 60-day public comment period closed
Dec. 3, 2019: NJDEP filed adoption package to OAL
Adoption includes a 1 year delayed operative date
  Current rules are in effect during this year
  Same timeframe municipalities have to update ordinances in accordance with MS4 permits

## Slide 5: Goals of the Amendments
Consistency
Predictability
Water Quality Improvements

## Slide 6: Existing Rule Layout
SUBCHAPTER 5. DESIGN AND PERFORMANCE STANDARDS FOR STORMWATER MANAGEMENT MEASURES
7:8-5.1 Scope
7:8-5.2 Stormwater management measures for major development
7:8-5.3 Nonstructural stormwater management strategies
7:8-5.4 Erosion control, groundwater recharge and runoff quantity standards
7:8-5.5 Stormwater runoff quality standards
7:8-5.6 Calculation of stormwater runoff and groundwater recharge
7:8-5.7 Standards for structural stormwater management measures
7:8-5.8 Maintenance requirements
7:8-5.9 Sources for technical guidance

## Slide 7: Rule Layout Re-arrangement
SUBCHAPTER 5. DESIGN AND PERFORMANCE STANDARDS FOR STORMWATER MANAGEMENT MEASURES
7:8-5.1 Scope
7:8-5.2 Stormwater management measures for major development
7:8-5.3 Nonstructural stormwater management strategies GI
7:8-5.4 Erosion control, groundwater recharge and runoff quantity standards
7:8-5.5 Stormwater runoff quality standards
7:8-5.6 Calculation of stormwater runoff and groundwater recharge
7:8-5.7 Standards for structural stormwater management measures
7:8-5.8 Maintenance requirements
7:8-5.9 Sources for technical guidance

## Slide 8: Amended Rule Layout
SUBCHAPTER 5. DESIGN AND PERFORMANCE STANDARDS FOR STORMWATER MANAGEMENT MEASURES
7:8-5.1 Scope
7:8-5.2 Stormwater management measures for major development
7:8-5.3 Green infrastructure
7:8-5.4 Groundwater recharge standards
7:8-5.5 Stormwater runoff quality standards
7:8-5.6 Stormwater runoff quantity standards
7:8-5.7 Calculation of stormwater runoff and groundwater recharge
7:8-5.8 Maintenance requirements
7:8-5.9 Sources for technical guidance

## Slide 9: Green Infrastructure Definition
A stormwater management measure that manages stormwater close to its source by:
Treating stormwater runoff through infiltration into subsoil;
Treating stormwater runoff through filtration by vegetation or soil, or
Storing stormwater runoff for reuse.

## Slide 10: Green Infrastructure Standard
GI BMPs must be used to satisfy recharge, quantity, and quality
3 Tables identifying the performance of each BMP in meeting the 3 standards
  Water Quality & Recharge – BMPs in Table 1
  Quantity – BMPs in Table 1 or Table 2
  If received a variance – BMPs in Table 1, Table 2, or Table 3
Maintain existing ability to propose an alternative stormwater design. Alternative design must meet GI definition and must meet drainage area limitation if similar to BMP with limit.

## Slide 11
Best Management Practice | Quality TSS removal rate (percent) | Quantity | Recharge | Minimum separation from seasonal high water table (feet)
Cisterns | 0 | Yes | No | -
Dry Wells | 0 | No | Yes | 2
Grass Swales | 50 or less | No | No | 2
Green Roofs | 0 | Yes | No | -
Manufactured Treatment Device (MTDs) | 50 or 80 | No | No | Dependent upon the device
Pervious Paving Systems | 80 | Yes | Yes No | 2 1
Small-scale Bioretention Systems | 80 or 90 | Yes | Yes No | 2 1
Small-scale Infiltration Basins | 80 | Yes | Yes | 2
Small-scale Sand Filters | 80 | Yes | Yes | 2
Vegetative Filter Strips | 60-80 | No | No | -
Table 1
Table 1 BMPs shall be used for recharge, quantity, and quality
Drainage area limitation applies to: dry wells, MTDs, pervious paving system, and small-scale bioretention, infiltration, and sand filters.
Table 1 only includes MTDs that meet the definition of GI

## Slide 12
Best Management Practice | Quality TSS removal rate (percent) | Quantity | Recharge | Minimum separation from seasonal high water table (feet)
Bioretention Systems | 80 or 90 | Yes | Yes No | 2 1
Infiltration Basins | 80 | Yes | Yes | 2
Sand Filter | 80 | Yes | Yes | 2
Standard Constructed Wetlands | 90 | Yes | No | N/A
Wet Ponds | 50-90 | Yes | No | N/A
Table 2
Table 2 BMPs may only be used for quantity
Wet ponds used under Table 2 must designed to have native vegetation and a reuse component

## Slide 13
Best Management Practice | Quality TSS removal rate (percent) | Quantity | Recharge | Minimum separation from seasonal high water table (feet)
Blue Roofs | 0 | Yes | No | N/A
Extended Detention Basins | 40-60 | Yes | No | 1
Manufactured Treatment Device | 50 or 80 | No | No | Dependent upon the device
Sand Filters | 80 | Yes | No | 1
Subsurface Gravel Wetlands | 90 | No | No | 1
Wet ponds | 50-90 | Yes | No | N/A
Table 3
Table 3 BMPs may only be used if a variance is granted

## Slide 14: Water Quality – Motor Vehicle Surface
The water quality standard will apply to motor vehicle surface instead of impervious surface
  Rule text will not require roofs or sidewalks to be treated – consistent with current implementation
  Will require pervious motor vehicle surfaces to be treated – consistent with scientific studies
Include in definition of major development

## Slide 15: Clarification to Applicability
Add definition of “regulated motor vehicle surface”
Add definition of “regulated impervious surface”
Change definition of major development to be 1 acre of disturbance, or ¼ acre of regulated impervious surface, or ¼ acre of regulated motor vehicle surface
Definitions of regulated motor vehicle surface and regulated impervious surface will include FAQ 10.2 (newly collected impervious surface and changes to existing drainage systems count as “new”)

## Slide 16: Clarification to Applicability
Require quantity, quality, and groundwater recharge to be met in each drainage area on-site (unless they converge before leaving the property)
Move mounding analysis requirement from recharge standard to apply to all infiltration BMPs

## Slide 17: CSO Related Changes
Clarify that water quality treatment is required for discharges into combined sewer systems
Clarify that water quantity control is required in tidal areas except discharges directly into lower reach of major tidal waterbodies
Create the option for a community basin, which will allow several properties in a CSS community to use a single large basin for quantity control
  Other standards must still be met on-site (including GI)

## Slide 18: Questions?